## Slide 1: PHOE 162-Introduction to Fiber Optics
Instructor: Dr. Elif Demirbas
Assistant Professor of Physics, Photonics and Optical Engineering
Bridgewater State University, Spring 2021

## Slide 2: Course Description
(2 credits) Corequisite: PHOE 162L Students will develop experience working with lasers, fiber optics and fiber optics applications that are commonplace for the photonics and optical technician. Fiber optics theory including index of refraction, materials, single and multi-mode operation, as well as typical fiber optics applications including cleaning, cleaving and splicing will be covered. One hour of lecture and two hours of laboratory weekly. Offered spring semester.

## Slide 3
Integrated Photonics Applications
PIC Components
Light Source: LED or Laser Diode
Modulator
Optical Fiber or Waveguide
Amplifier
Photodetector
1) Datacom/Telecon
2) Analog RF
3) Sensors
4) LiDAR/3D Display
https://www.wevolver.com/article/key-application-areas-for-integrated-photonics
Read more about integrated photonics applications

## Slide 4: Optical Fibers
An optical fiber is a flexible, transparent fiber made by drawing glass (silica) Typical diameter is slightly ticker than human hair.
Light is transferred between the two ends of the fiber.
Optical fibers are widely used in fiber-optic communications where they transmit information over long distances and at higher bandwidths than electrical cables.
https://www.google.com/search?q=optical+fiber&rlz=1C1GCEB_enUS866US868&sxsrf=ALiCzsaicfC6UcQJ4u2VE_VsGLrirtZbCQ:1651539595974&source=lnms&tbm=isch&sa=X&sqi=2&ved=2ahUKEwjehs23kML3AhUH2KQKHZW7BIkQ_AUoAnoECAIQBA&biw=1600&bih=789&dpr=1
See the images for Optical Fibers

## Slide 5: Fiber Structure and Mechanism
rcore:size of the core
rcladding :size of the cladding
An Optical Fiber Cable consists of core, cladding and buffer layers
At the most inner core, there is a core region with high refractive index material (n1) is surrounded by cladding region with low refractive index material (n2),
Light entering the fiber optical cable through core region undergoes total internal reflection at core-cladding interface
n1 > n2

## Slide 6: Light Modes
Light Modes are determined by n1 , n2, rcladding , rcore
If rcore is very small compared to rcladding, only one mode can pass, (single mode fiber).
When rcore is further increased, different modes can travel through the fiber(multimode fiber).
https://www.photonics.com/Articles/Fiber_Optics_Understanding_the_Basics/a25151

## Slide 7: Total Internal Reflection-Bucket of liquid
https://www.youtube.com/watch?v=0MwMkBET_5I

## Slide 8: Lab1-Laser Coupling to Single Mode Fiber

## Slide 9: Theory
Snell’s Law:
V-parameter
Cut-off wavelength
: core radius

## Slide 10: Objective
Instruments:
1 x Optical Bench
1 x Laser Diode (CPS635 or CPS532)
1 x Laser Power Supply (LDS5)
1 x Laser Safety Goggle (LG4)
1 x Convex lens (LA1608-A-ML)
1 x Iris (ID20)
1 x Power meter (PM16-130)
1 x Viewing Screen (EDU-VS1)
1 x Viewing Card (VRC2)
1 x Single mode fiber cable (P1-460B-FC-1)
2 x Ferule (FCM)
Posts, post holders (PH2, TR2, BA2)
Mounts (FCM, LMR1,KM100T)
Objective: Couple the laser light to a single mode fiber and calculate coupling efficiency
Include how many posts, post holders you are using each experiment

## Slide 11: Measurement
Measure the power after each component, laser, iris, lens
Measure Output and Input Power
Calculate the coupling efficiency
Pin : the power of light coming into one end of the fiber
Pout :the power of light coming out of other end of the fiber.
Coupling efficiency

## Slide 12: Lab report-
1) Objective
2) Introduction
3) Diagram
4) Instrumentation
Include the model name of the each components that you are using,
Check them from Thorlab website, you can include the pictures and explain in 2-3 sentences.
Include specs,
For example
for lens, focal length, diameter etc.
for fibers, NA, cladding radius etc.
5) Experimental Procedure (include steps, pictures etc.)
6) Results