## Slide 1: PHOE 162-Introduction to Fiber Optics
Instructor: Dr. Elif Demirbas
Assistant Professor of Physics, Photonics and Optical Engineering
Bridgewater State University, Spring 2021

## Slide 2
Integrated Photonics Applications
PIC Components
Light Source: LED or Laser Diode
Modulator
Optical Fiber or Waveguide
Amplifier
Photodetector
1) Datacom/Telecon
2) Analog RF
3) Sensors
4) LiDAR/3D Display
https://www.wevolver.com/article/key-application-areas-for-integrated-photonics
Read more about integrated photonics applications

## Slide 3
Final Presentation-April 15
Jean Bazile | Datacom/Telecom
Ryan Blanch | Datacom/Telecom
Claudia Cabrera | Datacom/Telecom
Kenneth Cardoso | Datacom/Telecom
Cameron Deluca | Analog RF
Shawn Fontilien | Analog RF
William Hernandez | Analog RF
Roshan Khadka | Sensors
Michael Prather | Sensors
Andrea Romig | Sensors
Fred Salazar | LIDAR/3D Displays
Gabe Woolf | LIDAR/3D Displays
Fiber Optic Use in Applications
Companies
Products
5-6 Slides

## Slide 4: Tentative Schedule
Week1
March 23-Introduction to Fiber Optics, Laser Safety Training
March 24-Laser to Single Mode Fiber Coupling, Group A-Experiment, Group B: Lab Report
March 25-Laser to Single Mode Fiber Coupling, Group B-Experiment, Group A: Lab Report
Week2
March 30- Multi-Mode Fiber, Group A-Experiment, Group B: Lab Report
March 31- Multi-Mode Fiber, Group B-Experiment, Group A: Lab Report
April 1- Fiber Coupler, Group A-Experiment, Group B: Lab Report
Week 3
April 6- Fiber Coupler, Group A-Experiment, Group B: Lab Report
April 7- Polarization Maintaining Fiber- Group A-Experiment, Group B: Lab Report
April 8- Polarization Maintaining Fiber- Group B-Experiment, Group A: Lab Report
Week4
April 13- 30-Loss in Fiber, Group A-Experiment, Group B: Lab Report
April 14- Loss in Fiber, Group B-Experiment, Group A: Lab Report
April 15-Final Day- 20 min Presentations.

## Slide 5
Polarization Maintaining (PM) Fiber
Polarization

## Slide 6
Polarization Maintaining (PM) Fiber
PM Fibers preserve the polarization of incoming light throughout the fiber
Polarization of input light and output light are the same

## Slide 7
Polarization Maintaining (PM) Fiber
Note that a polarization-maintaining fiber does not polarize light as a polarizer does. Rather, PM fiber maintains the linear polarization of linearly polarized light provided that it is launched into the fiber aligned with one of the fiber's polarization modes.

## Slide 8
Polarization Maintaining (PM) Fiber
Speed of the modes are different by using stress factors
https://www.youtube.com/watch?v=7rrb-_Iin-g

## Slide 9
https://en.wikipedia.org/wiki/Polarization-maintaining_optical_fiber
Polarization Maintaining (PM) Fiber Types

## Slide 10
Polarization Maintaining (PM) Fibers
PM Fibers preserve the polarization of incoming light throughout the fiber
Polarization of input light and output light are the same

## Slide 11
Polarization Maintaining (PM) Fibers
Bow Tie

## Slide 12: PM Fiber Cross Section

## Slide 13: Measurement of Polarization through PM fiber
Graph Output power vs polarizer angle

## Slide 14: Polarization Maintaining Fiber-Circularly Polarized
Instruments:
1 x Optical Bench
1 x Laser Diode (CPS635 or CPS532)
1 x Laser Power Supply (LDS5)
1 x Laser Safety Goggle (LG4)
1 x Convex lens (LA1608-A-ML)
2 x Iris (ID20)
1 x Power meter (PM16-130)
1 x Viewing Screen (EDU-VS1)
1 x Viewing Card (VRC2)
1 x Polarization Maintaining Fiber (P1-488PM-FC-1)
2 x Ferules (FCM)
1 x Quarter Wave Plate (before fiber)
1 x Polarizer (after fiber) (LPVISE100-A)
Posts, post holders (PH2, TR2, BA2)
Mounts (FCM, LMR1,KM100T, KM100)
Caliper

## Slide 15: Polarization Maintaining Fiber-Linearly Polarized
Instruments:
1 x Optical Bench
1 x Laser Diode (CPS635 or CPS532)
1 x Laser Power Supply (LDS5)
1 x Laser Safety Goggle (LG4)
1 x Convex lens (LA1608-A-ML)
2 x Iris (ID20)
1 x Power meter (PM16-130)
1 x Viewing Screen (EDU-VS1)
1 x Viewing Card (VRC2)
1 x Polarization Maintaining Fiber (P1-488PM-FC-1)
2 x Ferules (FCM)
1 x Half Wave Plate (before fiber)
1 x Polarizer (after fiber) (LPVISE100-A)
Posts, post holders (PH2, TR2, BA2)
Mounts (FCM, LMR1,KM100T, KM100)
Caliper

## Slide 16: Tips on laser alignment
Place a ruler in front of the laser, measure the height
Then, place the ruler further away from the laser, measure the height
The far field measurement should be the same with the near field measurement,
Adjust the knobs of the laser mount until the height of the laser beam is at the same height
on the ruler when ruler is further away

## Slide 17: Tips on how to couple laser on fiber core
Start with minimum iris aperture
Adjust the laser height (and the knobs on the laser mount) and iris height, so that the center of the laser beam is at the center of iris aperture
Adjust the mirrors in a way, that you see the laser beam going through the center of the second iris
Keep the lens flexible, do not fix on the bench.
Focus the laser beam at the core (center),
not around cladding only
You can change the height of the fiber
Move lens back and forth, right and left
(sometimes rotating helps too)
See the beam light from the same height of the fiber and work on the adjustment.
You can use the knobs on the laser beam for fine adjustment.

## Slide 18
Group A | Jean, Ryan, Claudia, Kenneth, Cameron, Shawn | 
Group B | William, Roshan, Michael, Andrea, Fred, Gabe |