## Slide 1: PHOE 162-Introduction to Fiber Optics
Instructor: Dr. Elif Demirbas
Assistant Professor of Physics, Photonics and Optical Engineering
Bridgewater State University, Spring 2021

## Slide 2
Integrated Photonics Applications
PIC Components
Light Source: LED or Laser Diode
Modulator
Optical Fiber or Waveguide
Amplifier
Photodetector
1) Datacom/Telecon
2) Analog RF
3) Sensors
4) LiDAR/3D Display
https://www.wevolver.com/article/key-application-areas-for-integrated-photonics
Read more about integrated photonics applications

## Slide 3
Final Presentation-April 15
Jean Bazile | Datacom/Telecom
Ryan Blanch | Datacom/Telecom
Claudia Cabrera | Datacom/Telecom
Kenneth Cardoso | Datacom/Telecom
Cameron Deluca | Analog RF
Shawn Fontilien | Analog RF
William Hernandez | Analog RF
Roshan Khadka | Sensors
Michael Prather | Sensors
Andrea Romig | Sensors
Fred Salazar | LIDAR/3D Displays
Gabe Woolf | LIDAR/3D Displays
Fiber Optic Use in Applications
Companies
Products
5-6 Slides

## Slide 4: Tentative Schedule
Week1
March 23-Introduction to Fiber Optics, Laser Safety Training
March 24-Laser to Single Mode Fiber Coupling, Group A-Experiment, Group B: Lab Report
March 25-Laser to Single Mode Fiber Coupling, Group B-Experiment, Group A: Lab Report
Week2
March 30- Multi-Mode Fiber, Group A-Experiment, Group B: Lab Report
March 31- Multi-Mode Fiber, Group B-Experiment, Group A: Lab Report
April 1- Fiber Coupler, Group A-Experiment, Group B: Lab Report
Week 3
April 6- Fiber Coupler, Group A-Experiment, Group B: Lab Report
April 7- Polarization Maintaining Fiber- Group A-Experiment, Group B: Lab Report
April 8- Polarization Maintaining Fiber- Group B-Experiment, Group A: Lab Report
Week4
April 13- 30-Loss in Fiber, Group A-Experiment, Group B: Lab Report
April 14- Loss in Fiber, Group B-Experiment, Group A: Lab Report
April 15-Final Day- 20 min Presentations.

## Slide 5
Instruments:
1 x Optical Bench
1 x Laser Diode (CPS635 or CPS532)
1 x Laser Power Supply (LDS5)
1 x Laser Safety Goggle (LG4)
1 x Convex lens (LA1608-A-ML)
1 x Iris (ID20)
1 x Power meter (PM16-130)
1 x Viewing Screen (EDU-VS1)
1 x Viewing Card (VRC2)
1 x Multi mode fiber cable (M42L01)
2 x Ferule (FCM)
Posts, post holders (PH2, TR2, BA2)
Mounts (FCM, LMR1,KM100T)
Caliper
Multi-Mode Fiber

## Slide 6: Multi-Mode Fiber
Very similar experiment,
Use multimode fiber
Alignment
Output light
Measure the power after each optical component
Calculate coupling efficiency
Note how many modes you see
Measure the diameter of modes

## Slide 7
Diagram

## Slide 8: Tips on laser alignment
Place a ruler in front of the laser, measure the height
Then, place the ruler further away from the laser, measure the height
The far field measurement should be same with the near field measurement,
Adjust the knobs of the laser mount until the height of the laser beam at the same height
on the ruler when ruler is further away

## Slide 9: Tips on how to couple laser on fiber core
Start with minimum iris aperture
Adjust the laser height (and the knobs on the laser mount) and iris height, so that the center of the laser beam is at the center of iris aperture
Keep the lens flexible, do not fix on the bench
Focus the laser beam at the core (center),
not around cladding only
You can change the height of the fiber
Move lens back and forth, right and left
(sometimes rotating helps too)
See the beam light from the same height of the fiber and work on the adjustment.
You can use the knobs on the laser beam for fine adjustment.

## Slide 10: Single Mode Fiber Coupler-next class
50:50, 75:25 and 90:10 fiber couplers.

## Slide 11: Alternative Setup to improve coupling coefficient
Instruments:
1 x Optical Bench
1 x Laser Diode (CPS635 or CPS532)
1 x Laser Power Supply (LDS5)
1 x Laser Safety Goggle (LG4)
2 x Convex lens (LA1608-A-ML)
2 x Iris (ID20)
2 x Mirrors
1 x Power meter (PM16-130)
1 x Viewing Screen (EDU-VS1)
1 x Viewing Card (VRC2)
1 x Multi mode fiber cable (M42L01)
2 x Ferule (FCM)
Posts, post holders (PH2, TR2, BA2)
Mounts (FCM, LMR1,KM100T, KM100)
Caliper

## Slide 12
Laser Safety Goggles, Check OD for the laser wavelength
Find the laser wavelength on the x-axis
Move up vertically until you hit the blue curve
From the blue curve, go horizontally to the y-axis
OD =1, reduces the laser power by 10 times
OD =2, reduces the laser power by 100 times
OD =3, reduces the laser power by 1000 times
And so on…
https://www.thorlabs.com/drawings/ec7ecd19cae82037-4C0DA3A8-91DD-7796-FD854A5A5621D702/LG4-SpecSheet.pdf
https://www.thorlabs.com/thorproduct.cfm?partnumber=LG4
LG4 : 12% visibility
LG4 :Spec Sheet, Optical Density vs Wavelength Graph
https://www.thorlabs.com/thorproduct.cfm?partnumber=LG13
LG13 : 39% visibility
https://www.thorlabs.com/drawings/ec7ecd19cae82037-4C0DA3A8-91DD-7796-FD854A5A5621D702/LG13-SpecSheet.pdf
LG13 :Spec Sheet, Optical Density vs Wavelength Graph

## Slide 13
Group A | Jean, Ryan, Claudia, Kenneth, Cameron, Shawn | 
Group B | William, Roshan, Michael, Andrea, Fred, Gabe |